## Slide 1: Ray Tracing by GPU
Ming Ouhyoung

## Slide 2: Outline
Introduction
Graphics Hardware
Streaming Ray Tracing
Discussion

## Slide 3: Introduction to Ray Tracing

## Slide 4: Why Use Programmable Graphics Cards
GPU vs. Chips specialized for ray tracing
  For the goal of providing maximum performance at the lowest cost, GPU can perform CPU-based algorithms without requiring fundamentally new hardware.

## Slide 5: Approach I
The Ray Engine [Graphics Hardware, 2002]
  use textures to hold the model and ray data
  use pixel shader to compute the intersection test
  the result are read back on to the AGP bus (bottleneck)

## Slide 6: Approach II
Ray Tracing on Programmable Graphics Hardware [ACM Transactions on Graphics, 2002]
  view a GPU as a general-purpose parallel/streaming processor
  map ray tracing onto a streaming model of computation

## Slide 7: Graphics Hardware

## Slide 8: Graphics Pipeline

## Slide 9: Ray Tracing Kernels
Eye Ray Generator
  produces a stream of viewing rays (pixels)
Traverser
  steps rays through the grid until the ray encounters a voxel containing triangles.
Intersector
Shader

## Slide 10: Traverser

## Slide 11: Intersector
Test ray intersections with all the triangles contained in the voxel.
2 types of output:
  If hit then output the ray and the triangle for shading.
  else pass the ray back to the Traverser and the search continues.

## Slide 12: Shader
If a ray terminates at this hit, then the color is written to the accumulated image.
may generate shadow or secondary rays and pass them back to the traversal stage.

## Slide 13: Streaming Ray Tracing

## Slide 14: Pixel Shader Architecture
Multipass Architecture
  Branching is implemented by loop
Branching Architecture
  requires only a single pass.
  requires significantly less bandwidth, and is compute-limited.

## Slide 15: Discussion
Acceleration data structures
  Static vs. Dynamic scenes
Multipass vs. Branching
CPU vs. GPU